## Slide 1: Number Conversion System
Decimal, Binary, Hexadecimal, Two’s Complement, and Signed Binary

## Slide 2: Number Conversion System Overview
We often use different number systems in computer science:
• Decimal (Base 10) – digits 0 to 9 (used in daily life)
• Binary (Base 2) – digits 0 and 1 (used inside computers)
• Hexadecimal (Base 16) – digits 0–9 and A–F (compact form of binary)

## Slide 3: Decimal → Binary (Integer)
Method: Repeatedly divide the decimal number by 2 and record the remainders.
Example: Convert 25₁₀ to binary:
25 ÷ 2 = 12 remainder 1
12 ÷ 2 = 6 remainder 0
6 ÷ 2 = 3 remainder 0
3 ÷ 2 = 1 remainder 1
1 ÷ 2 = 0 remainder 1
Read remainders from bottom to top → 11001₂
So, 25₁₀ = 11001₂

## Slide 4: Binary → Decimal (Integer)
Method: Multiply each bit by 2ⁿ (n = position from right, starting at 0) and add.
Example: Convert 10110₂ to decimal:
1×2⁴ + 0×2³ + 1×2² + 1×2¹ + 0×2⁰
= 16 + 0 + 4 + 2 + 0 = 22
So, 10110₂ = 22₁₀

## Slide 5: Fractional Decimal → Binary
Method: Repeatedly multiply the fractional part by 2 and track the integer parts.
Example: Convert 0.625₁₀ to binary:
0.625 × 2 = 1.25 → integer part 1
0.25 × 2 = 0.5 → integer part 0
0.5 × 2 = 1.0 → integer part 1
Collect integer parts in order → 0.101₂
So, 0.625₁₀ = 0.101₂

## Slide 6: Two’s Complement Binary → Decimal
Two’s complement is used to represent signed integers in binary.
Steps (for 8-bit example):
1. If MSB (leftmost bit) is 0 → number is positive, convert normally.
2. If MSB is 1 → number is negative:
a) Invert all bits (0↔1).
b) Add 1 to the result.
c) Convert to decimal and put a minus sign.
Example: 11101100₂ (8-bit):
Invert: 00010011₂; Add 1: 00010100₂ = 20₁₀ → result is −20
So, 11101100₂(two’s complement) = −20₁₀

## Slide 7: Signed Binary (Sign-Magnitude) → Decimal
In sign-magnitude representation:
• MSB is sign bit (0 = positive, 1 = negative).
• Remaining bits show the magnitude (absolute value).
Example (4-bit sign-magnitude): 1101₂
MSB = 1 → number is negative
Magnitude bits = 101₂ = 5₁₀
So, 1101₂ (sign-magnitude) = −5₁₀

## Slide 8: Decimal → Hexadecimal
Method: Repeatedly divide the decimal number by 16 and record the remainders.
Digits 10–15 are written as A, B, C, D, E, F.
Example: Convert 254₁₀ to hex:
254 ÷ 16 = 15 remainder 14
15 ÷ 16 = 0 remainder 15
Remainders (bottom to top): 15 (F), 14 (E) → FE₁₆
So, 254₁₀ = FE₁₆

## Slide 9: Hexadecimal → Decimal
Method: Multiply each hex digit by 16ⁿ and add (n = position from right, starting at 0).
Example: Convert 3AF₁₆ to decimal:
3AF₁₆ = 3×16² + A×16¹ + F×16⁰
A = 10, F = 15
= 3×256 + 10×16 + 15
= 768 + 160 + 15 = 943
So, 3AF₁₆ = 943₁₀

## Slide 10: Binary → Hexadecimal
Method: Group binary digits into sets of 4 bits from the right, then convert each group.
Each 4-bit group = 1 hex digit.
Example: Convert 110101110011₂ to hex:
Group: 1101 0111 0011
1101₂ = D₁₆, 0111₂ = 7₁₆, 0011₂ = 3₁₆
So, 110101110011₂ = D73₁₆

## Slide 11: Hexadecimal → Binary
Method: Replace each hex digit with its 4-bit binary equivalent.
Example: Convert 2F₁₆ to binary:
2₁₆ = 0010₂
F₁₆ = 1111₂
So, 2F₁₆ = 0010 1111₂